## Slide 1: Medical Ultrasound: Ergonomics

## Slide 2: Ergonomics- Definition
“Ergonomics (or human factors) is the scientific discipline concerned with the understanding of interactions among humans and other elements of a system, and the profession that applies theory, principles, data and methods to design in order to optimize human well-being and overall system performance”.
(International Ergonomics Association, 2014)

## Slide 3: Ultrasound
Ultrasound practitioners are generally considered predisposed to Work-Related Musculoskeletal Disorders (WRMSD) due to repetitive upper limb movements and static postures.
Diagnostic ultrasound presents multiple ergonomic concerns, including:
  Type and use of Equipment
  Scanning environment
  Work load
  Practitioner/patient factors

## Slide 4: Risks
Poor ultrasound practice ergonomics can lead to:
  Work-related Musculoskeletal Disorders (WRMSD)
  Absenteeism through ill health
  A significant economic burden

## Slide 5: Ultrasound WRMSD
WRMSD’s range in severity from pain and tingling to loss of function; acute, chronic and irreversible damage may lead to episodes of sickness from employment which carries a significant financial and social burden
  (Murphy & Coffin, 2002)
Between 80-90% of sonographers scan in pain
      (Baker 2001; Evans et al, 2010)
Anatomical regions commonly affected by WRMSD include:
    Shoulder
    Neck
    Wrist
    Back
    Hand/fingers
    Upper arm

## Slide 6: WRMSD-Scanning risks
Repetitive micro movements
Poor scanning posture
Sub standard equipment
Inefficient transducer grip
Excessive or sustained reaching
Application of force/pressure

## Slide 7: Work load risks
Increased referrals
Government waiting time targets
Staff shortages
Insufficient rest periods/breaks
Repetitive examination lists

## Slide 8: Practitioner risks
Aging workforce
Inappropriate environment/equipment set-up
Inappropriate moving & handling techniques

## Slide 9: Client risks
Increasingly obese population
  Displacement of adipose tissue in obese patients often requires increased probe pressure and stretching (HSE, 2012), this can elevate muscle fatigue and may lead to injury.

## Slide 10: Risk reduction of WRMSD in Ultrasound
Regular Health & Safety risk assessments
Appropriate equipment
Safe working environment
Moving and handling training
Education of risks of occupational injury
Appropriate equipment and ancillaries
Training and support.
Employers have a duty of care to provide regular health and safety risk assessments and an appropriate working environment for ultrasound practice. (SCoR & BMUS, 2015).

## Slide 11: Ultrasound Equipment
Ultrasound equipment specifications vary, however scanners should be:
  Mobile - Multidirectional wheels (scanner or cart)
  With the following credentials:
  Monitor- Fully adjustable height with swivel screen
  Transducer- Lightweight, flexible cables
  Console- Height adjustable with side tilt
  Operator controls- Well lit, Intuitive, logically arranged

## Slide 12: Ancillary equipment
Essential
Table - height adjustable
  Ultrasound table/couches should be height adjustable ideally by electronic control to allow operator to adjust appropriately throughout examination and in response to altered patient positions
Seat – ergonomically designed/adjustable
  Ergonomically designed chairs help relieve and prevent postural
  stress (Bambach, 2013)
Desirable
Arm/cable support
  Arm supports can be placed between the patient and practitioner
  to provide arm rest to reduce muscle loading in examinations (HSE,2012)
    Sagging cables should be positioned in cable supports to reduce wrist torqueing (SoR, 2006)
  Anti-fatigue mat
(Rothband, 2014 )

## Slide 13: Scanning Environment
Appropriate floor area to allow access around couch/flexible set-up
Black out blinds/windowless
Adjustable lighting
Air conditioning for ventilation and room cooling

## Slide 14: Good work practices
Appropriate work list scheduling
Adequate staffing levels
Apply due ergonomic consideration
  Adjust work environment prior to each scan (table height, chair height, patient position, lighting).

## Slide 15: Transducer Grip
Pinch Grip
Power grip
Employ the power grip
  The pinch grip is a common and natural approach to hold the US transducer however takes 4 to 5 more muscle and tendon force than the power grip and utilises only 25% of hand strength (Soundergonomics, 2014).

## Slide 16: Posture
Avoid or minimize twisting of the spine
Maintain an upright position
Avoid overreaching and unnatural positions
Limit arm abduction to less than 30˚
Scan with neutral wrist position

## Slide 17: Move and stretch
Rotate tasks
Take regular mini breaks
Stretch

## Slide 18: References
Baker, J.P., & Murphey, S.L., 2001. Minimizing workplace Injuries among Sonographers. Innovation in Ultrasound –Ergonomics Nov 2001 23-24
Bambach, 2013, The Bambach saddle seat. [online] Available at: http://www.bambach.co.uk/
Evans, K., Roll, S.C. and Baker, J., 2009, Work-Related Musculoskeletal Disorders (WRMSD)Among Registered Diagnostic Medical Sonographers and Vascular Technologists A Representative Sample. Journal of Diagnostic Medical Sonography Vol. 25, 287-299
GE, 2014, Ultrasound. [online] Available at: http://www3.gehealthcare.com/en/Products/Categories/Ultrasound
Health and Safety Executive, 2012, Risk management of Musculoskeletal disorders in sonography work. Date: 23 March 2012
International Ergonomics Association, 2014 [online] Available at: http://www.iea.cc/whats/index.html
Murphey, S,L. & Coffin, C,T., 2002, Ergonomics and Sonographer Well-being in Practice [online] Available at: http://www.soundergo.com/pdf/ErgSonWellBeing.pdf
Rothband, 2014, Cable support [online] Available at: http://rothband.com/product_info.php?cPath=109&products_id=234
Society of Radiographers, 2006, Industry standards for the prevention of work-related musculoskeletal disordered in sonography [online] Available at: http://www.sor.org/system/files/documentlibrary/public/sor_industrystandards_prevention_musculoskeletal.pdf
www.soundergonomics.com
Society and College of Radiographers and British medical Ultrasound Society, 2015, Guidelines for Professional Ultrasound practice [online]
Available: https://www.bmus.org/static/uploads/resources/GUIDELINES_FOR_PROFESSIONAL_ULTRASOUND_PRACTICE.pdf